## Slide 1
Surge Protection for the
City of Galveston
Advancing the Ike Dike Concept

## Slide 2: Report on $250K Galveston IDC monies
$250K spent specifically on surge modeling at Homeland Security Center of Excellence at Jackson State and A&M student salaries
Presentation today also includes results from other funding
A&M Matching Funds of at least $700K
Other Funding direct to A&M of about $700K
Bay Area Coastal Protection Alliance (BACPA) and other funding to A&M’s research partners
Monies obtained by and expended at the SSPEED Center
No State or Federal Monies

## Slide 3: Why Academic-led Surge Research
Lead Role in the Galveston Bay Region - Unique in US
Texas A&M Galveston and Rice Have Put Together Very Strong Teams
Initially TAMUG hoped to work with 6-County District but Delays in Funding and Their Restrictive Public Information Policies Have Made that Impossible
USACE Started Work in Galveston Bay ($4.4) but Redirected Work to Sabine and Brazoria; Trying to Begin Again with Texas Coast Project
But Even if They Do, the Traditional USACE Process Has Never Led to Large Surge Protection Projects
Instead Special Federal Legislation Has Caused Their Implementation

## Slide 4: Special Legislation Since 2005
USACE Funding Appropriated (million $) | 
P.L. 109-62 (FY2005 Hurricane Katrina | $400
P.L. 109-148 (FY2006 Hurricanes Katrina, Rita, Wilma, Ophelia | $2,361
P.L. 109-234 (FY2006) Hurricanes Katrina, Rita | $3,653
P.L. 110-28 (FY2007) Hurricanes Katrina, Rita | $1,433
P.L. 110-252 (FY2008-09) Hurricane Katrina (+ recent storms) At least | $5,762
P. L. 110-329 (FY2008) Hurricane Katrina (+ recent storms) At least | $1,500
P. L. 111-32 (FY2009) Hurricane Katrina (+ recent storms) At least | $439
P.L. 113-2 (FY2013) Hurricane Sandy | $5,081
Total $20,629B

## Slide 5
NOLA’s Surge Barrier is In Place

## Slide 6: Our Region’s Bottom Line
Other Hard-hit Areas Have Received Billions to Build Protection and to Plan Additional Protection
Ike Hit Us Hard and a Major Hurricane Hits the Upper Texas Coast about every 14 years - Its Been Almost 7 Years Since Ike – 10 since Rita
But There Have Been No Federal Expenditures in Galveston Bay to Protect the Petrochemical Capital of the US Despite its Strategic National Importance
The US Is Playing Russian Roulette with Galveston Bay
Aided by Those Trying to Delay Any Progress
We Should Feel a Sense of Urgency and of Outrage

## Slide 7: Probable Timing of Next Special Legislation
Can Hope for Proactive Legislation for Houston/Galveston
But Most Likely Will Be Reactive - Event Driven
Storm Event - Significant New Damage Anywhere in US
Large Request Requiring Special Legislation Event - Next Round of Sandy-Related Legislation, which May Be Soon - USACE has Completed $50M (No Match) Studies – Implementation Will Be Many Billions
Sandy Area Will Have a Plan – New Orleans Had a Very Rough Plan
We Will Need a Plan To Compete for Funds

## Slide 8: Our Research Goal Provide a Sound Basis for Special Legislation for the Galveston Bay Region As Soon As Possible
An Actionable Plan for Comprehensive Surge Protection of the Galveston Bay Region
And, with our implementation partners, Public Information in Support of this Plan and to help guide Special Congressional Legislation

## Slide 9: Our Strategy
Provide the Very First Cut at an Actionable Plan this Hurricane Season
Improve it and Re-release an Improved Version Every Year Until the Region Gets Congressional Legislation
Our Major Role Stops with Congressional Legislation
We want Congress to Instruct the USACE to Complete the Final Design, Build and Maintain the Protective Structure Elements of the Plan
The USACE, as They Did in New Orleans, Can Quickly Build an Effective Barrier Here; But It Will Require Special Legislation

## Slide 10: Who we are
Integrated Academic-led Research Team Investigating Multiple lines of Surge Defense – Including the Coastal Barrier
Researchers Devise an Actionable Plan and Provide Content to Implementation and Outreach Organizations
Wide Range of Public Support from Communities, Organizations, Businesses and Individuals

## Slide 11: TAMUG/SPEED Research Team
Economics
  Drs Bill Gilmer and Adam Perdue, Institute for Regional Forecasting, University of Houston
  Dr Hanadi Rifai, University of Houston
  Drs Sam Brody, Wes Highfield and Meri Davlasheridze, TAMUG
Surge Modeling
  Drs Robert Whalin, Tom Richardson and Bruce Ebersole; Homeland Security Center of Excellence, Jackson State University
  Dr Jeff Melby, USACE/Engineering Research & Development Center
  Dr Clint Dawson, The University of Texas
Barrier Design
  Dr Bas Jonkman, Delft Technical University
  Dr Jens Figlus, TAMUG
  Dr Phil Bedient, Larry Dunbar, Rice University
  Drs Galen Newman and Eric Bardenhagen, Landscape Architecture, TAMU
Overall Flood Risk Reduction/Project Coordination/Public Outreach/Data and Information Accessibility
  Dr Sam Brody, COL Len Waterworth and Dr Bill Merrell, TAMUG
  Dr Phil Bedient, Larry Dunbar, Jim Blackburn, Rice University

## Slide 12: Academic-led Research but Much More than Academics
Strong Implementation Partners and Supporters
Bay Area Houston Economic Partnership (BAHEP) and other economic partnerships – 12 endorsements
BAHEP – International Maritime Advisory Committee
BACPA – 501c3 – Supports Research and Public Outreach
Formal Endorsements from 22 Cities and Harris County Mayors and Councils Association
Formal Endorsement from the East Harris County Manufacturers Association (130+ Manufacturing Companies)

## Slide 13
Cities and organizations supporting the Ike Dike Concept

## Slide 14: Overall Galveston Bay Solution
Multiple Lines of Protection
Stop as Much Surge as Practicable Near the Coast
Coastal Barrier Risk Reduction (TAMUG-led)
Risk Reduction Measures Within the Bay (SSPEED-led)
Oyster reefs
Inflatable barriers

## Slide 15
Coastal Spine
Galveston Island
Bolivar Peninsula
Bolivar Roads
Intracoastal Waterway
• San Luis Pass
Existing Seawall
High
Island
Houston Ship Channel
The A&M-led strategy is to keep the ocean surge out of Galveston Bay using a gated coastal barrier
Notes: The critical need is to stop the surge at the coast – this protects the entire Bay area
1. Protects from catastrophic overflows and
2. Doesn’t allow the ocean surge into the Bay which in turn prevents massive internal surges

## Slide 16: HGAPS Alternatives

## Slide 17: Beach-the first line of defense

## Slide 18
The Sand Motor Concept

## Slide 19: Where We Are Towards a Very First Cut at an Actionable Plan
TAMUG Concentrating on Surge Reduction from the Coastal Barrier
Very First Cut Will Focus on Economics, in particular, a Preliminary but Credible Cost/Benefit Analysis of the Coastal Barrier
Cost/Benefit Is the Most Critical Aspect of Receiving Federal Funding
Expanding this Very First Cut into a More Rigorous Plan Will Require More than Local Funds

## Slide 20: National Research Council Report
Hard Structures Are Likely to Become Increasingly Important
No Solid Basis for 100 Year Level of Protection
Benefit-Cost Analysis Provides a Reasonable Framework for Evaluating Coastal Risk Management Investments
  Constrained by Acceptable Risk and Social and Environmental Dimensions

## Slide 21: Flood Risk and Optimization
Flood Risk=probability (per year) × consequences
Consequences: economic, life loss, environmental etc.
Various risk criteria: individual, societal risk, economic
Risk reduction benefits
Optimize level of protection
Economic optimization

## Slide 22: Optimizing barrier height
What is the optimal height of the storm surge barrier in terms of cost efficiency and damage prevention inside the basin?

## Slide 23: Determining Benefits
Preliminary HAZUS Damage Estimate Work Completed for 4 Storms
Need to Run More Storms – Determine Probabilities of Inundation in Region
Need to Add Petrochemical detail – UH Gilmer on Plant Value - SSPEED on Individual Plant Vulnerability and Storage Tank Vulnerability
Need to Add Business Disruption and Take Those Effects Nationally
Add Many Other Benefits – Environmental, Social, Flood Insurance
Some are Difficult to Monetize

## Slide 24: Preliminary Incomplete Surge Level and Economic Damage Analysis
ADCIRC and HAZUS Models

## Slide 25: Storm Surge Modeling
Defined a “Bracketing Set” of 25 Storms
  High-intensity hurricanes on various tracks
  Varying-intensity hurricanes on a single direct-hit track
Performed storm simulations for both existing and with-Ike Dike conditions
  Compared results to quantify storm surge suppression benefits
  Provided input to initial economic analysis
Developed improved understanding of Houston-Galveston regional storm surge response to hurricanes (open coast and in-bay)
  With and without the dike
  As a function of hurricane intensity and track

## Slide 26: Historic category 3, 4, 5 hurricanes (from NOAA )

## Slide 27: Hurricane Track Groupings and Storm Numbering
  21 hurricanes on different tracks (all 900 mb)
  4 hurricanes of varying intensity on a “direct hit” track (900, 930, 960 and 975 mb)

## Slide 28: Modeling Surge and Residual Bay Surge
How high can the surge get in various parts of the Galveston Bay system?
900-, 930-, and 960-mb storms on direct hit path to examine surge distribution with and without a 17ft above sea level coastal barrier
960-mb weak cat 3
930 cat 4 (1900 Storm about 936-mb)
900-mb very rare but possible - 900 off chart
930 mb
960 mb
900 mb ------------------------------------

## Slide 29: Path of Storms (Storm 122)
CP=900 mb
Rmax= 17.7 nm
Vf= 11 knots

## Slide 30: Surge Suppression for the 960-mb Direct Hit Storm
For this moderate hurricane, for existing conditions, surge in bay is 8 to 12 ft
With dike in place surges reduced to less than 4 ft; 6 to 9 ft of surge suppression
Existing
With-Dike
Difference

## Slide 31: Surge Suppression for the 930-mb Direct Hit Storm
Existing condition surges comparable to Ike
With dike in place, surges in bay reduced to 3-7 ft; surge suppression of 7-10 ft
Existing
With-Dike
Difference

## Slide 32: Surge Suppression for the 900-mb Direct Hit Storm
For this very extreme storm, in the bay, surges exceed Hurricane Ike surges by 5 to 7 ft – Catastrophic damage
With dike in place, surges reduced by 5 to 7 ft; still would have damage
Existing
With-Dike
Difference

## Slide 33: Relative Roles of the Coastal Barrier and Risk Reduction Measures Within the Bay
Before Quantitative Analysis Can Be Completed, Need to Examine Various Barrier Options and Model More Storms, But from This Example -
Coastal Barrier Is Effective in Reducing Surge in the Bay for All Storms
But for Some Severe Storms the Residual Bay Surge, Although Reduced, Will Be Damaging
In Bay Measures May Further Reduce This Residual Surge
In Bay Measures If Effective Could Also Reduce the Height Requirement for the Barrier
Complex Trade Offs – Economic, Environmental, Social

## Slide 34
900mb Storm Existing Residential Loss by Census Block
Notes: Note that we have one additional category (purple) where losses exceed 48 million.

## Slide 35
900mb Storm Protected Residential Loss by Census Block
Notes: Note that maximum loss is about 48 million while we also have fewer census block that recorded residential losses.

## Slide 36
Residential Loss Avoided (930mbStorm)
Notes: Note that maximum loss is about 48 million while we also have fewer census block that recorded residential losses.

## Slide 37
Existing
Protected
Difference

## Slide 38
Existing
Protected
Difference

## Slide 39
 | Existing | Protected
Residential | 5.32 | 1.60
Commercial | 2.21 | 0.63
Industrial | 5.54 | 2.00
Other | 0.50 | 0.15
Total Building Loss | 13.57 | 4.38
DRAFT Direct Economic Loss for Buildings by Land Use
900mb Storm
Notes: Our analysis shows significant reduction in losses. For example, for the largest of the four storms (Storm A), Residential building and content loss without a coastal spine was approximately $5.32 billion. This economic impact was reduced to $1.60 billion with coastal protection in place. In fact, residential economic losses reduced by almost 70% while the combined building loss reduced by almost 68% with the placement of a 17-foot dike along Galveston Island

## Slide 40: Determining Costs – Coastal Barrier
Water Barrier – Bolivar Roads Gate System Is By Far the Major Component of Cost
Soil Conditions for Water Barrier Foundations Biggest Unknown
Land Barrier – Fortified Dunes
Raising Coastal Highways Is an Option

## Slide 41: Land Barrier Solutions
Msc thesis N. West
Texas A&M (Bardenhagen and Newman)
Delft Student Team
TU Delft, prelim.

## Slide 42: Bay Hydraulics - 2D – Depth Integrated (M. Ruijs, 2011)
Impact of barrier
  Tidal Amplitude
  Current (shipping)
  Salinity (oyster, shrimp)
  Need 3-D Model

## Slide 43: Water Barrier Solution
Navigation section
Environmental section

## Slide 44: Bolivar Roads barrier: environmental section (P. de Vries)
Main challenge: foundation

## Slide 45: Bolivar Roads barrier: navigational section
Main challenges:
Hinge, dynamics, control
c
Structural analysis

## Slide 46: Operation barrier: closure

## Slide 47: Barrier dynamic stability (J. Smulders)
  Roll angle governing during swing operation
  Rubber supports required to ensure barge is not damaged at landing
  Additional measures required in case of negative head

## Slide 48
Flood
Risk
Reduction
Surge/Flood Modeling
Make available FEMA 10/100/500yr without protection max water surface elevation files.
Extend barrier up towards Sabine to prevent flow around.
Select proxy storm for each recurrence interval.
Run (3) with protection.
Exchange IKE max water surface elevation.
Additional named storms:
Ike, re-track Ike, re-track Carla, 1900 storms (short term).
● SSPEED has previous named storms (Katrina, Rita, Isaac, Ike done @ P7).
Carla and 1900 will be done with JSU winds (P7).
● 1900 hurricane wind and pressure
Probabilistic Storms: Assess which storms are important to run-ruling out, which storms can eliminate because of insignificant damage (900-975).
Assess alternatives based on same FEMA storms.
Examine different barrier heights.
Save wave spectrum at San Luis and Bolivar.
Research Action Items
From Flood Risk Reduction Meeting (Dec. 15th-16th, 2014)
Barrier Design
Water Barrier:
● Delft-Cost Estimate by spring
a. Bigger opening for navigation
b. Scour protection issues
c. Soil issue, need cores (LT)
d. Alternative environmental Barrier
e. Flow and fish larvae issues
f. Overflow, leakage during storm
● Nice visualization needed
Land Barrier
● Estimates of alternative costs based no different heights.
● Examine alternative construction designs/costs.
● Better understand sand availability and costs.
● Decide on placement of barrier (beachfront vs. road).
● Visualization
Bay Interior
● Visualization
● Land use issues
● Buy out targets
● (MT) “Charrette” working with nature to design barriers within the bay.
● SSPEED leads interior efforts, and decides when we all get involved.
Economics
Finish populating HAZUS model-residential: Run for IKE
Finish Industrial dataset and integrate into model.
Develop a detailed written document for surge model-economic interface.
Run storms without protection for baseline economics.
Damage assessment for storms with complete data (total damage) for protection scheme.
IMPLAN Analysis
Land use change analysis?
(M/LT) loss of life analysis
Economic benefit of constructing the barrier or other alternatives: development, tourism, ecosystem services (MT).
Lower insurance payments and claims.
(M/LT) costs for different elevations and connect to return periods.
Maintenance, operational cost issues.
TAMU/TAMUG
Dutch
SSPEED Center
Jackson State
U. of Houston

## Slide 49: Summary
Coastal Barrier (Ike Dike) Greatly Reduces Surge Damage for All Storms
A 17ft high barrier would “handle” most storms
Well on Our Way to a Preliminary Cost/Benefit Analysis and a Very First Cut at an Actionable Plan
Strong Research Team and Plans in Place to Continuously Improve the Actionable Plan
Will Need To Raise Additional Resources to Continue Our Work

## Slide 50: What You Can Do! Take Pride that Your City Started All This
Get Angry and Stay Angry
Demand Galveston Bay Be Treated Like Other Hard-Hit Areas
Recognize that Our Region Has Already Overwhelming Supported a Surge Suppression Approach that Features the Coastal Barrier
Realize that Special Congressional Legislation Will Be Necessary
Push for an Actionable Plan to Help Such Legislation
Acknowledge that Now Only Academic-Led Researchers with Local Funding Are Working to Produce a Plan
Urge Additional Funding Be Focused on Progress Toward Achieving Federal Legislation
Work with State and Federal Officials and Legislators to support Surge Suppression for the Galveston Bay Region As Soon As Possible